UNIVERSITY OF HUDDERSFIELD – FIRE RISK ASSESSMENT

| B: Fire Fighting Equipment |
| --- |
| Building |  | Area |  | Assessed by |  | Date |  |
|  | Yes | No | Comments |
| 1 | Is there sufficient fire fighting equipment provided? |  |  |  |
| 2 | Is the fire fighting equipment appropriate to the fire hazards present? |  |  |  |
| 3 | Is the fire fighting equipment appropriately located? |  |  |  |
| 4 | Is the fire fighting equipment subject to regular maintenance, undertaken by competent personnel and is recorded? |  |  |  |
| 5 | Are there procedures in place to identify and replace defective fire fighting equipment? |  |  |  |
| 6 | (Other – please state) |  |  |  |

| B: FIRE FIGHTING EQUIPMENT - GUIDANCE |
| --- |
| TYPES |
| Fire fighting equipment will range from fire extinguishers, hose reels, fire blankets and gas suppression systems. |
| Fire Risk | Type of Equipment |
| General (paper, wood, fabrics etc.) | Water, foam, hose reel |
| Flammable/highly flammable liquids | Foam, dry powder |
| Cooking activities | Dry Powder, fire blanket |
| Electrical equipment | Carbon dioxide, dry powder |
| Archived material | Gas suppression system |
| LOCATION AND COVERAGE |
| Fire extinguishers and hose reels will generally be located on means of escape. As a general guide to ensure adequate coverage, at or close-by each fire alarm call point – where two call points within same lobby area can just be one – there should be a nine litre water and two kilogram carbon dioxide extinguisher. Where there are specific fire hazards (e.g. areas where flammable/highly flammable liquids are used or stored, cooking activities are taking place or high concentration of electrical equipment) that particular area will have its own dedicated fire fighting equipment. |
| MAINTENANCE |
| Extinguishers must be subject to an annual service, five-yearly discharge/recharge test and replacement every 20 years. Hose reels must be serviced to the appropriate standard annually. All maintenance must be undertaken by competent personnel. In addition to individual record label on equipment, a separate record must be maintained for all equipment. Arrangements must be in place for the regular checking (monthly) of the general condition of fire fighting equipment. Systems must be in place for the reporting of used or damaged equipment, the remedying of the fault and providing temporary coverage whilst this is being done. |